## Slide 1: RIDOT’s Wrong-Way Driving Mitigation Program

## Slide 2: Pilot Detection Systems
Wrong Way Detection Systems on 24 locations
  Worked with State Police to pinpoint locations
  Citation/incidents – corridors chosen
  Side-by-side ramps, isolated off-ramps, and confusing geometry.
  All solar powered/wireless systems
Goal – to provide active feedback to the:
  Wrong-way driver via flashing signage
  Right-way drivers via Dynamic Message Signage
  TMC/RI State Police

## Slide 3: Pilot Detection Systems
Wrong-Way Alert Generated
  Offending vehicle tracked 100’ by incoming radar
  Offending vehicle crosses camera trip line
  Offending vehicle detected by outgoing radar
Once all three conditions are satisfied, alert is sent

## Slide 4: Wrong-Way Vehicle Alert – Web-Based System Alert

## Slide 5: Alert Protocol
RIDOT
  Alert via website at RIDOT TMC
  Email sent to TMC
  TMC locate vehicle on overhead camera (if available)
  TMC and police make phone contact
  TMC activates DMS sign (if available)
  Police and TMC coordinate resolution
State Police
  Alert via website at State Police
  TMC and police make phone contact
  Police dispatched
  Police and TMC coordinate resolution
Notes:   RIDOT’s Message - WRONG WAY DRIVER REPORTED – USE CAUTION

## Slide 6: Pilot Overview
Cost
  $2.2 Million
Effectiveness
  100+ wrong-way events since May 2015
  Resulted in no fatalities or reported crashes
  Allowed for data driven approach to geometric improvements.
Maintenance
  Added 100K annual funds to existing on-call ITS Maintenance contract
System Testing
  Individual systems tested if no alert received within 60 days
  All detection systems tested annually, regardless of alerts received